## Plant Monitor Automatic Watering System with Web Control
### Overview
This project combines a soil moisture sensor, ESP32 microcontroller, BC547-driven relay, water pump, and an LCD display to create a plant watering system with both automatic and manual control via a local web interface.

### Hardware Components
- ESP32 microcontroller
- Soil moisture sensor (analog)
- BC547 transistor (to drive relay safely)
- Relay module (controls water pump)
- Water pump (DC)
- I²C LCD (16x2)
- Power supplies:
  - ESP32 + LCD: regulated 5V
  - Pump: separate 5V or 12V supply depending on pump specification
- Wiring considerations:
  - Keep SDA/SCL short and twisted
  - Use pull-up resistors (4.7k–10kΩ) if LCD module lacks them
  - Include a flyback diode across pump to prevent voltage spikes

### Software & Libraries
- Arduino IDE (programming environment)
- Libraries:
  - WiFi.h (for ESP32 WiFi connectivity)
  - WebServer.h (simple local web server)
  - Wire.h and LiquidCrystal_I2C.h (LCD display)

### Functional Achievements
1. Automatic watering logic:
  1. Reads soil moisture using analog sensor and smooths data.
  2. Triggers watering if moisture < 30%.
  3. Intermittent watering cycles:
    1. Pump ON for 6s, OFF for 12s (3 cycles).
    2. Stops watering automatically if moisture > 40%.
2. Manual web override:
  1. ESP32 hosts local web page accessible via browser (same WiFi).
  2. Displays:
    1. Current soil moisture (%)
    2. Pump state (ON/OFF)
    3. Mode (AUTO/MANUAL)
  3. Buttons for manual control:
    1. Manual ON
    2. Manual OFF
    3. Return to AUTO mode
3. LCD Display:
  1. Shows current moisture reading and pump state.
  2. Updates every ~500ms.
  3. Avoids garbled characters by ensuring stable power and clean I²C signals.
4. Hardware improvements:
  1. BC547 transistor ensures safe relay switching.
  2. Separate power lines for pump vs. ESP32/LCD prevent voltage dips.
  3. Flyback diode prevents relay-induced spikes.
5. Networking:
  1. ESP32 connects to local 2.4GHz WiFi.
  2. Serves simple HTML web interface.
  3. Fully local, no cloud dependencies.

### System Logic Summary
Variables:
- smoothedMoisture: filtered moisture reading
- pumpRunning: current state of pump during automatic cycles
- manualOverride: true if user clicked manual ON/OFF
- manualPumpState: tracks manual pump state
- cycleCount: counts intermittent watering cycles (max 3)
- pumpOnTime / pumpOffTime: defines ON/OFF duration per cycle (currently 6s/12s)
Automatic Mode:
1. If manualOverride is false and moisture < 30%: start watering.
2. Pump cycles ON/OFF 3 times (6s ON, 12s OFF) or until moisture > 40%.
3. LCD and web page reflect current state.
Manual Mode:
1. Clicking ON/OFF sets manualOverride = true.
2. Pump state follows manual input immediately.
3. Clicking AUTO button clears manualOverride, resuming automatic logic.
4. LCD and web page reflect manual control.
Hysteresis:
Automatic watering avoids constant toggling by only stopping if moisture > 40%.
Web Page Logic:
- Root (/) shows moisture, pump state, mode, and buttons.
- Manual ON/OFF and AUTO routes change state and redirect back to root page.
- Connection header close ensures redirects work reliably.

### Notes & Observations
- Longer ON times were temporarily used for testing fluid flow through long tubing (6s ON / 12s OFF). These can be adjusted later for actual plant watering.
- LCD issues with garbled characters were caused by voltage dips and I²C noise; solved with stable power and wiring improvements.
- Fully local system: ESP32 serves web page without cloud dependency.
- System can later be upgraded with live data logging or graphing using a local server if desired.

### Next Steps / Upgrades
1. Integrate automatic + manual override fully (already done).
2. Optional: add live page refresh using WebSockets.
3. Optional: add data logging to SD card or local server.
4. Adjust watering times for actual plant needs.
5. Expand to multiple pumps/sensors if desired.